## Slide 1: Capacitive Switch Sensor ICs
Capacitive
Switch
ROHM capacitive switch ICs utilize a proprietary capacitance detection circuit to achieve both high noise immunity and high sensitivity. Stable detection of minimal changes in capacitance allows for reliable sensing of finger contact, even when using thicker enclosures and protective films.
Features
Achieves high noise immunity and sensitivity
Integrated LED dimming, press and hold, and auto calibration functions
Built-in noise cancellation, offset cancellation, and temperature drift cancellation functions
Supports matrix configuration of sensor electrodes
Applications
Printers, TVs, Audio Players, and Other Consumer Products
Home Appliances/Equipment (i.e. Refrigerators, AC, Air Purifiers)
Office Automation
VQFN020V4040
(4.0×4.0×Max.1.0mm)
Clears Stringent Noise Tests
IEC61000-4-6 equivalent
Judgement Criteria: No malfunctions
Pass
Noise Removal
ROHM
±10V
BU21079F
Capacitive
Touch
Controller
Function
Generator
Sine Wave
0.1 to 2MHz(1kHz steps)
2 to 80MHz(10kHz steps)
Amplitude : 20V(±10V)
Class-leading* noise immunity
*ROHM October 2018 study
High Sensitivity Contributes to Greater Design Flexibility
Overlay Thickness(Acrylic Plate)
ROHM
15mm
High
Sensitivity
Improved design flexibility makes
it possible to add
switches to
curved
surfaces
High sensitivity detection not affected by noise
Overlay Thickness
Electrodes
Block Diagram
(Sensor)
BU21170 : 5ch
BU21072 : 10ch
BU21078 : 12ch
BU21077 : 8ch
BU21079 : 8ch BU21181 : 18ch
BU21182 : 20ch
(LED)
BU21170 : 5ch
BU21072 : 6ch
BU21078 : 8ch
BU21077 : －
BU21079 : －
BU21181 : －
BU21182 : －
LDO28
POR
AFE_CNT
MPU
VREF
LDO15
OSC
WDTR
C/V
Converter
Sensor
AFE
PRDR
WRAM
LEDDRY
PWM-CNT
Host
I/F
DTG
LOGIC
AFE
A/D
VDD
Single power
supply
operation
SDA
SCL
TEST
VSS
AVDD
DVDD
SIN0-9
SIN0-5
INT
Touch!
Electrode(PCB)
Control Panel Button
Simplifies Noise
Countermeasures